Switching
Gihan Dias
CS2032
2011S3 – Aug 2013

---
Outline
- Types of Network
- Switching
- Circuit Switching
- Message Switching
- Packet Switching
  - Virtual circuit switching
  - Datagram switching
  - Label Switching

---
Types of Network
Unswitched
  - Point-to-point
  - Multi-point
  - Broadcast
Switched

---
Why Switched Networks?
3 nodes
3 links
4 nodes
6 links
5 nodes
10 links
10 nodes - ? links

---
Why Switched Networks?
- Not cost effective to have all nodes DIRECTLY connected to all other nodes
- Unlike LANS, the nodes could be spread out and vast in number (can’t broadcast the signal)
- The signal can be switched from sender to receiver

---
Switching: abstract model
output
input
Number of connections: from few (4 or 8) to huge (100K)

---
Why switching?
- To get signals to the correct destination
- Needed when source and destination are not directly connected
  - e.g. travelling by bus
Used when network is large in size or number of stations

---
Routing and Switching
Routing
  - Identifies the route traversed by data to get from source to destination
Switching
  - Transfers data from one network / link to another

---
Types of switching
- Circuit switching
- Message switching
- Packet switching
  - Virtual circuit
  - Datagram

---
Circuit Switching
- A dedicated communications path is pre-allocated
- This requires the caller, callee and all intervening links and nodes to be available at the same time
- Once established, circuit capacity must be paid for, whether or not it is used

---
Circuit Switching
The route, once it is set up,
  - has low transmission delays (good)‏
  - cannot be optimised (bad)‏
- Suits human-to-human telephone communications
- Less suitable for computer communications
  - Set up time
  - Cannot handle data bursts

---
Types of Circuit Switching
Space-division switching
  - Each call takes a different path through the switch
Time-division switching
  - Each call is divided into small pieces and each piece is assigned a time-slot
  - The contents of each time-slot are switched independently

---
Space Division Switch

---
Space division switching
- Each sample takes a different path through the switch, depending on its destination
- Crossbar: Simple space-division switch
- Crosspoints can be turned on or off
i
n
p
u
t
s
outputs

---
Crossbar - example
sessions: (1,2) (2,4) (3,1) (4,3)
output
1
2
3
4
1
2
3
4
inputs

---
Time-Division Switching
Multiplexor: aggregates sessions
  - N input lines
  - Output runs N times as fast as input
Demultiplexor: distributes sessions
  - one input line and N outputs that run N times slower
Can cascade multiplexors
De-Mux
1
2
N
1
2
N
1 2 N
Mux

---
Time Slot Interchange (TSI) : example
sessions: (1,3) (2,1) (3,4) (4,2)
1
2
3
4
2
1
4
2
1 2 3 4
3 1 4 2
3 1 4 2
1
3
3
4
write to shared memory and read in different order

---
Problems with Circuit Switching
Efficiency
  - The circuit may be idle much of the time
  - especially in computer communications
Delay
  - time needed to set up the circuit
  - but low delay once circuit is set up

---
Delays in Circuit-Switch Network

---
Message Switching
- Entire messages sent store-and-forward, hop-by-hop
- Message makes intermittent progress as each hop becomes available
- End-to-end delivery time cannot be guaranteed
- Very long messages can:
  - hog buffer space at intermediate nodes
  - hog the links between them

---
Packet Switching
Network comprises a set of nodes (switches or routers)‏
  - intermediate stations
Connected by links
  - point to point
  - broadcast
D
Broadcast
NW
E
router
B
F
G
H2
A
H1
host
Pt-Pt
link
C

---
Packet Switching (cont.)‏
- Data stream is divided into packets
- Each packet comprises data and a header
Data Stream
100100011100101000011110101101011110001
Packet 1
Header Data
Packet 2
Header Data
Packet 3
Header Data
1011110001
101111
00001111010110
101100
100100011100101
101101

---
Packet Switching (cont.)‏
Data sent from one host to another
  - end stations
- Each intermediate station switches each incoming packet through a link to another node
- Packets make their way through the network from node to node and finally to their destination

---
Packet Switching
router
D
B
packet
E
H2
A
H1
host
C

---
Types of Packet Switching
- Virtual Circuit Switching
- Datagram Switching
- Label Switching

---
Virtual Circuit Packet Switching
- Connection set up between end stations before data is transferred
- the packets are sent along a pre-chosen route
Set-up delay before sending data

---
Virtual-Circuit Identifier
- Each packet is assigned to a virtual circuit
- Each VC has a Virtual Circuit Identifier
- Different VCIs on each link
Dr. J M Garrido
Fall 2009

---
Dr. J M Garrido
Fall 2009

---
Datagram Packet Switching
- Packets are routed independently
- No initial circuit set-up costs or delays
- Switching each packet is relatively expensive
- adapts to node and link failures during transmission
- datagrams may arrive out of order

---
A Datagram Switch
A switch in a datagram network uses a routing table that is based on the destination address.
The destination address in the header of a packet in a datagram network remains the same during the entire journey of the packet.
Dr. J M Garrido
Fall 2009

---
Label Switching
- Route at edges – Switch in core
- A Label is attached to each packet when it arrives at a label switched network
- Each core switch switches the packet based on the label, and then substitutes a new label for the next hop

---
Label Switched Network

---
Switching Strategies
message progress under each main strategy:
time:

---
Summary
- Types of Network
- Circuit Switching
- Message Switching
- Packet Switching
  - Virtual circuit switching
  - Datagram switching
  - Label Switching