## Slide 1: Introduction to communications
Sulochana
CS2032 – Principles of Computer Communication

## Slide 2: Lesson Outcomes
After successful completion of this lesson you will be able to:
  List down the generic components of a communication network
  Illustrate the layered network architecture
  Describe the functions of each layer of the OSI model

## Slide 3: 1. Communication
Sending information from one place to another
Transmission of signals that will be interpreted as data
An information could be transmitted electronically between two points over a physical connection medium
Human voice,
Human visualization
Telegraph
1837
1876
Morse Code
Telephone

## Slide 4: 1.1 Types of Communication
Video, Text, Voice, Data, Multimedia
Direction of Information Flow
  One-way
  Interactive – Non real time
  Interactive – Real time
Number of parties involved
  Two-party
  Multi-party

## Slide 5: 2. Network
A system that connects devices for communication:
  PSTN: Public Switched Telephone Network
  LAN: Local Area Networks
  Television Network
  Vehicular Networks
  Internet

## Slide 6: 2.1 Components of a Network
Terminals for Access
Equipment for Switching
Media for Transmission

## Slide 7: 2.2 How to study a Network

## Slide 8: 2.3 Challenge
Different architecture
Different languages
Different data formats
Different communication rates
Modularization
Layering
Standardization

## Slide 9: 3. Layered Architecture
Separate functions
Transparent Implementation
  Flexible to modify
  Independent design and testing
E.g: OSI Reference Model, TCP/IP Model

## Slide 10: 4. OSI Model
Open System Interconnect (OSI)
  Communication regardless of underlying architecture
7 Layers
  Layer – well defined function
  Boundaries – minimum information flow across

## Slide 11: 4.1 Physical Layer
Purpose
  Accept a raw string of bits and deliver it across a link
Functions
  Encoding and signaling
  Data transmission and reception
  Topology and physical network design
Hardware Specifications – operations of cables, connectors, wireless radio transceivers, network interface cards and other hardware devices

## Slide 12: 4.2 Data Link Layer
Purpose
  Provide error free transmission across a single link
Functions
  Data framing
  Error Detection and handling
  Flow Control
  Addressing – hardware level

## Slide 13: 4.3 Network Layer…cntd
Purpose
  Deliver packets (datagrams) from sender to the receiver (host-to-host) across a communications network
  Shield higher layers from the details of how packets got to their destination

## Slide 14: 4.3 Network Layer
Functions
  Logical Addressing
    Which machine to send the packet to
  Routing
    How to get there
  Datagram encapsulation
  Congestion Control
    Lot of packets in the network core
  Quality of Service
    Guarantee levels of service

## Slide 15: 4.4 Transport Layer
Purpose
  Provide end-to-end delivery from one host to the other
Functions
  Connection establishment, management and termination
  Multiplexing and demultiplexing
  Error detection and correction
  Flow Control
  Quality of Service

## Slide 16: 4.5 Session Layer
Purpose
  Provide a means of controlling the dialog between two end-users (applications)‏
Functions
  Dialog Control (full vs half duplex)‏
  Token Management
  Synchronisation
  Recovery Management
Not often implemented in real systems

## Slide 17: 4.6 Presentation Layer
Purpose
  Formatting data for transmission
Functions
  Translation
  Compression
  Encryption
In practice not implemented in a separate layer but included elsewhere – e.g. in the applications

## Slide 18: 4.7 Application Layer
Purpose
  Provide network based applications to users
File transfer, Electronic Mail, World Wide Web, Virtual Terminal, Instant Messaging, Directory Services, Remote file systems
Some widely used applications are standardized

## Slide 19: 4.8 A Quick Recap
Credit to : http://ccna-cisco.webs.com/osiiiii.png

## Slide 20: 4.9 OSI Layers in Operation

## Slide 21: 4.10 Communication in OSI Model
http://www.supportsages.com/blog/wp-content/uploads/2010/09/Osi_layer.png

## Slide 22: 5. CS 2032 - Scope
Physical Layer in depth
Touches DLL
Introduce briefly Network layer and Application layer

## Slide 23: 5.1 CS2032
Principles of Computer Communications
  Data Communications
Course Outline
Mode of Delivery
  Lectures
  Tutorials
  Labs
Assessment
  CA % Exam %

## Slide 24: 5.2 Course Outline

## Slide 26: 6. Revision
List down the generic components of a communication network.
What are the layers in OSI model?
Write down a functionality per each layer.

## Slide 27: Thank you